TRIBHUVAN UNIVERSITY

INSTITUTE OF ENGINEERING

Pulchowk Campus

Thesis No.: 064/MSI/S/614

Performance Analysis of MIMO Detectors

By

Sagun Manandhar

064/MSI/S/614

Thesis

Submitted to

Masters of Science in Information and Communication Engineering,

Department of Electronics and Computer Engineering

January, 2011

Performance Analysis of MIMO Detectors

By

Sagun Manandhar

064/MSI/S/614

Thesis Supervisor

Asst. Prof. Daya Sagar Baral

A thesis submitted in partial fulfillment of the requirements for the

degree of Master of Science in Information and Communication

Engineering

Department of Electronics and Computer Engineering

Institute of Engineering, Pulchowk Campus

Tribhuvan University

Lalitpur, Nepal

January, 2011

COPYRIGHT ©

The author has agreed that the library, Department of Electronics and Computer Engineering, Institute of Engineering, Pulchowk Campus, may make this thesis freely available for inspection. Moreover the author has agreed that the permission for extensive copying of this thesis work for scholarly purpose may be granted by the professor(s), who supervised the thesis work recorded herein or, in their absence, by the Head of the Department, wherein this thesis was done. It is understood that the recognition will be given to the author of this thesis and to the Department of Electronics and Computer Engineering, Pulchowk Campus in any use of the material of this thesis. Copying of publication or other use of this thesis for financial gain without approval of the Department of Electronics and Computer Engineering, Institute of Engineering, Pulchowk Campus and author’s written permission is prohibited.

Request for permission to copy or to make any use of the material in this thesis in whole or part should be addressed to:

Head

Department of Electronics and Computer Engineering

Institute of Engineering

Pulchowk Campus

Lalitpur, Nepal

Recommendation

The undersigned certify that they have read and recommended to the Department of Electronics and Computer Engineering for acceptance, the thesis entitled “Performance Analysis of MIMO Detectors”, submitted by Mr. Sagun Manandhar in partial fulfillment of the requirement for the award of the degree of “Master of Science in Information and Communication Engineering”.

………………………………………………….

Supervisor: Asst. Prof. Daya Sagar Baral

Department of Electronics and Computer Engineering,

Institute of Engineering,

Tribhuvan University,

Pulchowk, Nepal.

………………………………………………….

External Examiner: Er. Bimal Acharya

Departmental Acceptance

The thesis entitled “Performance Analysis of MIMO Detectors”, submitted by Mr. Sagun Manandhar in partial fulfillment of the requirement for the award of the degree of “Master of Science in Information and Communication Engineering” has been accepted as a bonafide record of work independently carried out by him in the department.

----------------------------------------------------------

Prof. Dr. Shashidhar Ram Joshi

Head of the Department

Department of Electronics and Computer Engineering,

Institute of Engineering,

Tribhuvan University,

Pulchowk, Nepal.

# ACKNOWLEDGEMENT

This dissertation would not have been possible without the guidance and the help of several individuals who in one way or another contributed and extended their valuable assistance in the preparation and completion of this study.

This thesis “Performance Analysis of MIMO Detectors” is the title of my thesis. I owe my deepest gratitude to my thesis supervisor Asst. Prof. Daya Sagar Baral for his insightful advices and valuable suggestions, as well as his consistent encouragement throughout the whole time of this thesis.

I would like to thank the Program Coordinator of Masters of Science in Information and Communication Engineering Asst. Prof. S. K. Ghimire for his suggestions and guidance.

I would like to thank Prof. Dr. Shashidhar Ram Joshi, Head of Department, Department of Electronics and Computer Engineering for providing the students of MSICE engineering with this special opportunity to show the glance of what our institute has brought in us.

I would like to thank the Department of Electronics and Computer Engineering, Kathmandu Engineering College for providing me the computer lab where I did most of my research and simulation works.

Also, I thank Digital Outreach Pvt. Ltd team for their support and inspiration throughout my study period.

I have no words to thank my parents, siblings and my friends for their support and endless love throughout my life. Lastly, I offer my regards and blessings to all of those who supported me in any respect during the completion of the thesis.

Sagun Manandhar
064/MSI/614

# ABSTRACT

During these years, Multiple Input Multiple Output (MIMO) has become a popular technique in wireless communication. However, despite of advances in electronics, receiver design and battery life, the complexity of MIMO systems still remains an issue which is a limitation over more widespread use of this technology. Hence simplifications in receiver design and improvement in the performance of simple architectures have become a key issue in current MIMO technology research.

In wireless communication, Multipath fading is constantly limiting and challenging the ability to achieve the full potential of wireless communications. Since the transmitted power is regulated and bandwidth is precious, there’s need for techniques which requires no additional bandwidth and transmitted power. Diversity techniques are very powerful techniques that makes use of two or more copies of a signal and combine those signals to combat multipath fading.

Among many diversity techniques known, space diversity technique is very popular due to simplicity and bandwidth efficiency. Space diversity can be implemented in both the transmitting end as well as the receiving end. This thesis provides detail explanations of space diversity technique. The emergence of transmit diversity led to the evolution of Multiple Input Multiple Output (MIMO) systems. The decoding section is an indispensable part of MIMO systems. This thesis compares the Block Error Rate (BER) performance of various MIMO decoding schemes like Zero forcing (ZF), Minimum Mean Squared Error (MMSE), Maximum likelihood (ML), Linear Least Square Estimation (LLSE), and ZF-VBLAST by performing various simulations.

Finally, when there is a presence of strong line of sight (LOS), Rician fading channel is appropriate for modeling the channel. This fact motivated the comparison between the various MIMO decoding schemes under Rayleigh and Rician channel environments in this thesis.

# TABLE OF CONTENTS

ACKNOWLEDGEMENT	vi

ABSTRACT	vii

TABLE OF CONTENTS	viii

LIST OF FIGURES	xi

ABBREVIATIONS	xiv

1. INTRODUCTION	1

1.1 Introduction	1

1.2 Objective	4

1.3 Scope of Thesis	5

2. LITERATURE REVIEW	6

2.1 Wireless Communication	6

2.2 Space Time Coding	7

2.2.1 Space-Time Processing For Wireless Communication	8

2.3 The Wireless Channel Model	9

2.4 Diversity	10

2.4.1 Time Diversity	10

2.4.2 Space Diversity	10

2.4.3 Pattern Diversity	11

2.4.4 Frequency Diversity	11

2.4.5 Polarization Diversity	11

2.4.6 Angular Diversity	11

2.5 Modulation	12

2.5.1 BPSK	12

2.5.2 QPSK	14

3. MULTIPLE-INPUT MULTIPLE-OUTPUT COMMUNICATIONS	16

3.1 Introduction to MIMO	16

3.1.1 MIMO System Equation	17

3.1.2 Channel Model	18

3.2 Spatial Multiplexing Detection	19

3.2.1 Linear Detection	19

3.2.1.1 Zero Forcing	19

3.2.1.2 Minimum Mean Squared Error	20

3.2.1.3 Linear Least Square Error	20

3.2.2 Optimal Detection	21

3.2.2.1 Maximum Likelihood	21

4. V-BLAST ARCHITECTURE	23

4.1 Introduction to V-BLAST	23

4.1.1 System Overview	25

4.2 V-BLAST Detection	25

5. METHODOLOGY	28

5.1 Overall Algorithm:	28

5.2 ZF-VBLAST Algorithm	28

5.2.1 Interference Nulling	29

5.2.2 Interference cancellation	29

5.2.3 Ordering	30

6. SIMULATION AND RESULTS	32

6.1 Experimental Setup	33

6.2 Results	35

6.2.1 Results obtained from simulation with BPSK source at input.	35

6.2.2 Results obtained from simulation with QPSK source at input.	40

6.2.3 Comparison of Linear / Optimal / VBLAST with BPSK source.	45

6.2.4 Comparison of Linear / Optimal / VBLAST with QPSK source.	49

6.2.5 Performance comparison of modulation techniques for different channels.	53

6.2.6 Performance comparison in terms of channel with different modulation schemes.	58

7. DISCUSSION	63

8. LIMITATION	65

9. CONCLUSION	66

10. FUTURE RECOMMENDATIONS	67

10.1 Approach suitable for higher constellations	67

10.2 Investigations for other fading channels	67

10.3 Group detection	67

10.4 Ordering	67

References	68

Bibliography	70

# LIST OF FIGURES

Figure 1 : A generic MIMO communication system model	3

Figure 2 : Constellation diagram of BPSK	13

Figure 3 : Constellation diagram of QPSK	15

Figure 4 : A MIMO Communication System Model	16

Figure 5 : V-BLAST schematic diagram	24

Figure 6 :  Experimental setup for simulation purpose	34

Figure 7 : BER performance curve of ZF receivers in Rayleigh Channel	35

Figure 8 : BER performance curve of ZF receivers in Rician Channel	35

Figure 9 : BER performance curve of MMSE receivers in Rayleigh Channel	36

Figure 10 : BER performance curve of MMSE receivers in Rician Channel	36

Figure 11 : BER performance curve of LLSE receivers in Rayleigh Channel	37

Figure 12 : BER performance curve of LLSE receivers in Rician Channel	37

Figure 13 : BER performance curve of ML receivers in Rayleigh Channel	38

Figure 14 : BER performance curve of ML receivers in Rician Channel	38

Figure 15 : BER performance curve of ZF-VBLAST receivers in Rayleigh Channel	39

Figure 16 : BER performance curve of ZF-VBLAST receivers in Rician Channel	39

Figure 17 : BER performance curve of ZF receivers in Rayleigh Channel	40

Figure 18 : BER performance curve of ZF receivers in Rician Channel	40

Figure 19 : BER performance curve of MMSE receivers in Rayleigh Channel	41

Figure 20 : BER performance curve of MMSE receivers in Rician Channel	41

Figure 21 : BER performance curve of LLSE receivers in Rayleigh Channel	42

Figure 22 : BER performance curve of LLSE receivers in Rician Channel	42

Figure 23 : BER performance curve of ML receivers in Rayleigh Channel	43

Figure 24 : BER performance curve of ML receiver in Rician Channel	43

Figure 25 : BER performance curve of ZF-VBLAST receivers in Rayleigh Channel	44

Figure 26 : BER performance curve of ZF-VBLAST receiver in Rician Channel	44

Figure 27 : BER performance curve in Rayleigh Channel for 2-2 MIMO link	45

Figure 28 : BER performance curve in Rician Channel for 2-2 MIMO link	45

Figure 29 : BER performance curve in Rayleigh Channel for 3-3 MIMO link	46

Figure 30 : BER performance curve in Rician Channel for 3-3 MIMO link	46

Figure 31 : BER performance curve in Rayleigh Channel for 4-4 MIMO link	47

Figure 32 : BER performance curve in Rician Channel for 4-4 MIMO link	47

Figure 33 : BER performance curve in Rayleigh Channel for 5-5 MIMO link	48

Figure 34 : BER performance curve in Rician Channel for 5-5 MIMO link	48

Figure 35 : BER performance curve in Rayleigh Channel for 2-2 MIMO link	49

Figure 36 : BER performance curve in Rician Channel for 2-2 MIMO link	49

Figure 37 : BER performance curve in Rayleigh Channel for 3-3 MIMO link	50

Figure 38 : BER performance curve in Rician Channel for 3-3 MIMO link	50

Figure 39 : BER performance curve in Rayleigh Channel for 4-4 MIMO link	51

Figure 40 : BER performance curve in Rician Channel for 4-4 MIMO link	51

Figure 41 : BER performance curve in Rayleigh Channel for 5-5 MIMO link	52

Figure 42 : BER performance curve in Rician Channel for 5-5 MIMO link	52

Figure 43 : BER performance curve of ZF detector in Rayleigh Channel	53

Figure 44 : BER performance curve of ZF detector in Rician Channel	53

Figure 45 : BER performance curve of MMSE detector in Rayleigh Channel	54

Figure 46 : BER performance curve of MMSE detector in Rician Channel	54

Figure 47 : BER performance curve of LLSE detector in Rayleigh Channel	55

Figure 48 : BER performance curve of LLSE detector in Rician Channel	55

Figure 49 : BER performance curve of ML detector in Rayleigh Channel	56

Figure 50 : BER performance curve of ML detector in Rician Channel	56

Figure 51 : BER performance curve of ZF-VBLAST detector in Rayleigh Channel	57

Figure 52 : BER performance curve of ZF-VBLAST detector in Rician Channel	57

Figure 53 : BER performance curve of ZF detector with BPSK source	58

Figure 54 : BER performance curve of ZF detector with QPSK source	58

Figure 55 : BER performance curve of MMSE detector with BPSK source	59

Figure 56 : BER performance curve of MMSE detector with QPSK source	59

Figure 57 : BER performance curve of LLSE detector with BPSK source	60

Figure 58 : BER performance curve of LLSE detector with QPSK source	60

Figure 59 : BER performance curve of ML detector with BPSK source	61

Figure 60 : BER performance curve of ML detector with QPSK source	61

Figure 61 : BER performance curve of V-BLAST detector with BPSK source	62

Figure 62 : BER performance curve of V-BLAST detector with QPSK source	62

# ABBREVIATIONS

MIMO	Multiple Input Multiple Output

SISO	Single Input Single Output

MISO	Multiple Input Single Output

VLSI	Very Large Scale Integration

DSP	Digital Signal Processing

MAI	Multiple Access Interference

CCI	Co-Channel Interference

CSI	Channel State Information

WLAN	Wireless Local Area Network

CDMA	Code Division Multiple Access

DSL	Digital Subscriber Lines

BER	Block Error Rate

SNR	Signal to Noise Ratio

VBLAST	Vertical Bell Labs Layered Space Time

ZF	Zero Forcing

MMSE	Minimum Mean Square Error

LLSE	Linear Lease Square Error

ML	Maximum Likelihood

ZF-VBLAST	Zero Forcing VBLAST

BPSK	Binary Phase Shift Keying

QPSK	Quadrature Phase Shift Keying

ISI	Inter Symbol Interference

SMD	Spatial Multiplexing Detection

3G	Third Generation System

AWGN	Additive White Gaussian Noise

EGC	Equal Gain Combining

SC	Selection Combining

Tx	Transmitter

Rx	Receiver

# 1. INTRODUCTION

## 1.1 Introduction

In the recent years, with the advances in Very Large Scale Integration (VLSI) and Digital Signal Processing (DSP) technologies have enabled the implementation of complex algorithms and coding systems in small devices with low power consumption, as required in the modern mobile communications. Such technical breakthroughs have promoted to the rapid growth of the global market in wireless communication equipment. Furthermore, the demands for higher bandwidth capacity and improved performance of wireless communications are continuously growing day by day. With the advent of applications such as multimedia data transmission (audio and video streaming), online gaming networks, a much higher spectral efficiency is required to provide the services with tolerable quality [1].

In wireless channels, ambient noise is one of the major problems which arise due to thermal movement of electrons within the antenna. Propagation losses, another important issue in wireless channel, occur in the form of diffusive losses, caused by the open nature of wireless channels and shadow fading, which results due to the obstruction made by objects such as buildings, walls, trees, hills etc. Multipath, which refers to the phenomenon where multiple copies of a transmitted signal are received at the receiver, this arises due to reflection from various objects which create multiple radio link between the transmitter and the receiver. Interference, is also a significant concern in many wireless channels, it is typically one of two types: multiple-access interference (MAI) and co-channel interference (CCI). Interference arising from other signals in the same network is categorized as multiple access interference whereas co-channel interference refers to interference from signals from different networks, but operating at the same frequency band.

In addition to all these challenges, there is an increasing demand for higher data rates, better quality of service, and higher network capacity. To meet all these needs there is a requirement for new technique that improves the spectral efficiency and increase the reliability of the system side by side.

The MIMO (Multiple Input Multiple Output) technology promises a cost effective way to provide these capabilities. A MIMO system consists of a wireless communication link with multiple numbers of antenna elements on both the transmitter and receiver side. MIMO technology takes advantage of the multipath scenario by sending a single transmission from the transmitter antenna array to bounce along multiple paths to the receiver. Thus transmitting data on multiple signal paths increases the amount of information transferred within a system. Thus the system will be able to handle more information and at a rate faster than a SISO (Single Input Single Output) scenario with a single path.

MIMO concepts have been under development since many years for both wireless and wire‐line systems. One of the earliest MIMO‐to‐wireless communications applications came in 1984 with groundbreaking developments by Jack Winters of Bell Laboratories. This pioneered MIMO described ways to send data from multiple users on the same frequency / time channel using multiple antennas at the transmitter and receiver. Since then, several academics and engineers have made significant contributions in the field of MIMO.

Many WLAN, Wi‐Max, and cellular companies offer (or are planning to offer) MIMO‐based solutions. Existing applications include multiple‐antenna systems, Code Division Multiple Access (CDMA) systems used in 3G cellular systems, and even Digital Subscriber Lines (DSL) with multiple telephone lines experiencing crosstalk.

MIMO was developed in the early 1970s by the researchers at Bell Laboratories. It was thought to be unfeasible during that era because of the high expense occurring in generating the processing power and time necessary to handle the MIMO signals. However today, with so much advancement in technology and cost reductions in signal-processing schemes and with the needs to meet the increasing demands, the researchers are compelled to research and develop MIMO for wireless systems.

Figure 1 : A generic MIMO communication system model

A general MIMO communication system model is as shown in Figure 1. The input bit streams are coded and modulated to generate symbol streams. This output is launched into the MIMO channel through N transmitting antennas. The signal is received by M receiver antennas and processed by the decoder.

MIMO is certainly an emerging cost-effective technology that promises significant improvement in capacity. Research conducted worldwide in various institutions reveals that MIMO is the preferred technology for future wireless mobile communication.

However, the promised improvements resulting from the use of MIMO come with a large increase in system complexity. Hence, simplifications in MIMO architecture and improvements for the performance of simple architectures have become key issues in the current researches. Research studies that target simple and efficient MIMO systems are rapidly emerging. The particular areas considered range from the study of efficient transmitter and receiver design, improved coding schemes, antenna design, equalization issues, and networking issues to the realization of MIMO system into practice.

This thesis primarily focuses on the study and simulation of various processing techniques that can be employed to provide improvements in receiver performance in a fading single-user MIMO wireless communication environment. The performance of various spatial multiplexing detection methods are compared in terms of block-error rate (BER).

## 1.2 Objective

This thesis focuses on the study and simulation of MIMO receivers and the performance of various MIMO receivers such as zero forcing, minimum mean squared error, linear least square error and maximum likelihood are compared in terms of block error rate (BER) for the Rayleigh and Rician channel environment with BPSK and QPSK modulation at the input. Some special detection algorithm has been proposed for MIMO system and VBLAST is one of them. Among the various VBLAST algorithms, ZF-VBLAST algorithm has been considered in this thesis. VBLAST algorithm uses iterative method to detect symbols.

The main objectives of the thesis are:

- To study the MIMO system.

- Simulation of transmit and receive diversity in BPSK modulation with Rayleigh and Rician fading model for the ZF, MMSE, LLSE and ML receiver as proposed in [2] as a basic requirement for the thesis work.

- To use a higher modulation technique, QPSK for bandwidth efficiency than that of BPSK.

- To study MIMO VBLAST receiver.

- To compare the performance of ZF/VBLAST receiver, ZF receiver, MMSE receiver, LLSE receiver and ML receiver under Rayleigh and Rician channel with BPSK and QPSK modulation techniques.

## 1.3 Scope of Thesis

The scope of the works presented in this thesis focuses on the comparison of the different detection techniques that can be used in the receiver side in terms of Block Error Rate (BER) via simulation in MATLAB.

Among the various spatial multiplexing detection techniques discussed in the thesis, Maximum Likelihood (ML) detection is the optimal detection technique but the computation complexity grows enormously with an increase in the number of antennas in the system. Zero-Forcing (ZF), Minimum Mean Squared Error (MMSE) and Linear Least Square Estimation (LLSE) are other detection techniques which are sub optimal but are relatively simple being linear detection techniques.

V-BLAST is another type of detection technique which incorporates an ordering scheme and detects the signal in an iterative manner with linear detection techniques like ZF used at each stage.

# 2. LITERATURE REVIEW

## 2.1 Wireless Communication

Wireless communication is the transfer of information over a distance without using electrical conductors or wire. Wireless Communication is the most rapidly evolving areas in the field of communication today. Recent researches and advances in wireless communication systems have dramatically increased the throughput through wireless channels and also the reliability. Hence wireless communication is most widely used today. The major advantages of wireless communication are seamless mobility, portability and accessibility.  Although wired communication is more stable, reliable and better in terms of performance, it comes with the limitation of being bound to a fixed location.  Therefore, there is always a need to get rid of the fixed wires [3].

Two fundamental aspects of wireless communication that makes the problem challenging and interesting is fading and interference. However, wired line communications are immune to these phenomenons. Fading can be defined as the variation of channel strength over time and frequency. The variation can be divided into two parts, as large scale fading and small scale fading. Large scale fading is due to the path loss of signal as a function of distance and shadowing by large objects such as buildings and hills. This is typically frequency independent. Small scale fading is due to the constructive and destructive interference of multiple signal paths between the transmitter and receiver [4].

Variations in the received signal from various components of the transmitted signal that are propagated over different paths are known as multipath fading. So multipath fading must be handled properly in order to minimize the effect. One solution for minimizing this problem is to increase the transmit power but increasing transmit power is a difficult solution because of various constraints. Very useful solution comes from the concept of diversity.  Diversity is used where two or more inputs at the receiver are used to get uncorrelated signals [9]. Previously in conventional wireless communications, a single antenna is used at both the source and the destination.  Such configuration gives rise to problems due to multipath effects. During the transmission, when the signal is obstructed by hills, buildings etc they are scattered, and thus takes many paths to reach to the destination. The delayed arrival of scattered portions of the signal causes problems such as fading and discontinuous reception. In data transmission system such as wireless internet, data speed is reduced and number of error is increased. The use of two or more antennas at the source and the destination eliminates the trouble caused by multipath wave propagation. In particular, researchers have shown that schemes with multiple antennas on both sides can tremendously enhance the system’s throughput, reliability and coverage, without the necessity of extra power and bandwidth [5].

## 2.2 Space Time Coding

Space-time coding is a coding technique designed to be used with multiple transmit antennas. Coding is performed in both spatial and temporal domains to introduce correlation between signals transmitted from various antennas at different time periods. The spatial-temporal correlation is used to exploit the MIMO channel fading and minimize transmission errors at the receiver. Space-time coding can achieve transmit diversity and power gain over spatially uncoded systems without sacrificing the bandwidth [6]. There are various approaches in coding structures but the concern in all these schemes is the exploitation of multipath effects in order to achieve high spectral efficiencies and performance gains.

Space time coding (STC) rely on transmitting multiple, redundant replica of the signal to the receiver. Multiple, redundant copies are sent so that, all of them fade simultaneously and only a few of them survives the physical path in a good enough state so that they can be reliably decoded. By the use of multiple transmit antenna, space–time code (STC) dramatically improves the reliability of data transmission in wireless communication systems.

Space–time coding is a communication technique for wireless systems that employs multiple transmitter antennas and a single or multiple receiving antennas. Information theory has been used to demonstrate that multiple antennas have the potential to dramatically increase the achievable data rates. Space–time codes realize these gains by introducing temporal and spatial correlation into the signals transmitted from different antennas. There is, in fact, a diversity gain that results from multiple paths between base station and mobile terminal, and a coding gain that results from how symbols are correlated across transmit antennas. Significant increase in throughput is possible with only two antennas at the base station and one or two antennas at the mobile equipment, with simple receiver structures. The second antenna at the mobile terminal can be used to further increase system capacity through interference suppression [7]. The article provided in [7] provides an overview of space–time coding techniques and the associated signal processing framework for narrowband and broadband wireless communications.

The main objective of space-time codes is to obtain maximum diversity as far as possible. Space-time codes provide a diversity gain equal to the product of the number of transmitter and receiver antennas. An effective and practical way to approach the capacity of multiple-input multiple-output (MIMO) wireless channels is to employ space-time (ST) coding [8].

### 2.2.1 Space-Time Processing For Wireless Communication

Space time processing refers to the signal processing performed in the spatial and temporal domain on the signals received or transmitted from an antenna array, in order to improve performance of wireless networks [6]. Main problems in the wireless communications such as co-channel interference due to cellular frequency reuse, multipath fading decreases system quality and capacity. By using space-time processing, that is adding more antenna at receiver or transmitter, system performance can be improved. Briefly, space-time (ST) processing can improve network capacity, coverage and quality by reducing co-channel interference (CCI) while enhancing the diversity and array gain.

Using extra space component (more receive or transmit antenna) enables interference cancelation in a way that is not possible with single antenna systems. The desired signal and CCI almost always arrive at the antenna array with distinct and well separated spatial signatures, thus allowing the system to exploit this difference to reduce CCI. Moreover, ST transmit systems can use spatial selectivity to transmit signals to desired mobile device while minimizing interference from other mobiles, i.e., smart antenna systems. Additionally, ST processing in the receiver can be used to increase diversity gain and suppress inter-symbol interference (ISI). In the next topic, wireless channel model will be introduced, to be familiar with the degradation effects of wireless channels.

## 2.3 The Wireless Channel Model

The propagating radio signals are affected by the physical channel in various ways [6]. A signal propagating through the wireless channel usually arrives at the receiver from different paths, referred as multipath. These paths arise from scattering, reflection and refraction of the signals from surrounding objects. The received signal is much weaker than the transmitted version due to the effects of path-loss, slow fading (long-term fading) and fast fading (short-term fading). Multipath propagation results in the spreading of the signal in different dimensions. These are delay (time) spread, Doppler (or frequency) spread and angle spread. In free space propagation, path- loss can be easily found. Fading can be calculated as multiplication of both short and long term fading components.

Slow fading can be characterized by a distribution which is affected by antenna heights, operating frequencies and type of environment. One of the most prominent statistical models is Okamura model. Fast fading component has Rayleigh density function if there is no direct path from signaling parts. Rayleigh distribution is as follows,

If there is a presence of direct path, fast fading component will have Rician density function, which is as follows,

Effects of multipath in small scale fading are detailed in [15].

## 2.4 Diversity

Diversity is an efficient method to combat the multipath fading. The key idea behind diversity is to obtain many replicas of transmitted signals at the receiver. It is very difficult to obtain all the replicas of these signals perfectly at the receiver because different replicas fade independently. Thus, the receiver can decode the transmitted signal using these replicas that is received [9]. To obtain diversity, different methods can be adopted in reality, which is discussed below.

### 2.4.1 Time Diversity

When different time slots are used for diversity, it is called time diversity. Independent fades can be obtained if two time intervals are separated for more than the coherence time and with this fact different copies of transmitted signal are sent through separated time slot. These phenomena of time diversity can be described as using a repetition code. If signals representing the same information are sent over the same channel at different time slots it is time diversity and it is used in system that suffers from burst errors.

### 2.4.2 Space Diversity

The concept of space diversity is that the antenna should be spaced far enough apart so that different received copies of the signal undergo independent fading, so that at least any one of the copy of signal may not suffer from deep fading. In space diversity no additional work is required on the transmission end, and no additional bandwidth or transmission time is required but the physical constraints which are associated with it may limit this application. This feature of space diversity completely differentiates it from frequency diversity and time diversity. The spacing is an important factor in space diversity [4]. Fading is different at different points on the earth surface, so two antennas placed a few wavelengths, apart will have uncorrelated fading and this is the secret of space diversity.

### 2.4.3 Pattern Diversity

In pattern diversity there are of two or more co-located antennas, but these co-located antennas has different radiation patterns. Directive antennas are used in this type of scheme that is usually physically separated by a distance apart. Compared to that of single Omni directional antenna, it can provide higher gain.

### 2.4.4 Frequency Diversity

Fading are different at different frequencies so frequency diversity is used. Different carrier frequencies are used to transmit the same signal. To achieve diversity, the carrier frequencies should be separated by more than the coherence bandwidth of the channel. Frequency diversity suffers from bandwidth deficiency because different frequency is used to transmit the replica of a signal. Frequency means bandwidth which is very precious. Also the receiver needs to tune to different carrier frequencies [10].

### 2.4.5 Polarization Diversity

The signals may go through multiple reflections, resulting in the change of polarization of transmitted signal due to transmission media. By utilizing two complementary polarizations, this diversity scheme can minimize a system from polarization mismatches. This reduces the signal fading caused by polarization mismatch.

Polarization diversity has proven valuable for mobile communication at base stations because of the fact that base stations are susceptible to the near random orientations of transmitter antennas. Normally polarization is used in mobile base stations with radiating element separated by apart.

### 2.4.6 Angular Diversity

Angular diversity uses directional antennas to achieve diversity so that the different copies of the transmitted signal are collected from different angular directions. These different signals collected from different angles travels along different paths and all signals will not suffer from deep fading. Unlike multiple antennas, it doesn’t need separate physical locations like using multiple antennas so it is also very good for small devices [10]. An angular diversity radiating system is described for troposphere scatter radio links.

## 2.5 Modulation

Modulation is the process of encoding information from a source in a manner suitable for transmission. Modulation may be done by varying the amplitude, phase or frequency of a high frequency carrier in accordance with the amplitude of the source message [6]. This section describes the various modulation techniques used in the thesis.

### 2.5.1 BPSK

BPSK uses two points on the constellation diagram. It lies totally in one axis i.e. x-axis. It has no y-axis projection. The vector flip-flops on x-axis depending on the value of bit [16]. It does not particularly matter exactly where the constellation points are positioned. This modulation is the simplest of all the PSK modulation techniques. It’s drawbacks is that it can only modulate at one bit/symbol and so is inappropriate for the cases where  high data-rate is required and the bandwidth is limited.

In BPSK, the phase of a constant amplitude carrier signal is switched between two values according to two possible signals m1 and m2 corresponding to binary 1 and 0, respectively. If sinusoidal carrier has an amplitude Ac and energy per bit, then transmitted BPSK signal is either [15].

for (binary 1)

Or,

=		 for (binary 0)

It is often convenient to generalize m1 and m2 as binary data signal, which takes on one of the two possible shapes of the pulse. Then the transmitted signal may be expressed as

From this expression, the constellation diagram can be drawn as shown in the figure below.

Figure 2 : Constellation diagram of BPSK

From the constellation diagram, it can be seen that the distance between adjacent points in the constellation is.  Using this in the average probability of bit error in additive white Gaussian noise (AWGN), the average probability of bit error is obtain as Where  is the noise spectral density.

### 2.5.2 QPSK

Quadrature phase shift keying (QPSK) uses four constellation points, and each point is equispaced around a circle as shown in the figure 2.2. Advantage of using four points or four phases, it can encode two bits per symbol. In QPSK, information is conveyed through phase variations, so that in each time period, the phase can change only once. Since there are four possible phases, there are 2 bits of information conveyed within each time slot.

In QPSK, phase of the carrier takes on one of the four equally spaced values, such as  where each of the value corresponds to a unique pair of message bits. The QPSK signal for this set of symbol states may be define as [16]

Where Ts is the symbol duration and is equal to twice the bit period.

Using Trigonometric identities

If basic function  and  are define over interval   for the QPSK signal set, then four signals in the signals in set can be expressed in terms of the basis signal as

Based on this representation, QPSK signal can be represented using a 2-D constellation-diagram with four points as show in the figure below.

Figure 3 : Constellation diagram of QPSK

Distance between adjacent points in QPSK constellation diagram is. Since each symbol corresponds to two bit, then, thus the distance between two neighboring points in the QPSK constellation is equal to. Using this in the average probability of bit error in additive white Gaussian noise (AWGN), the average probability of bit error is obtained as

Similarly the Probability of symbol error rate for QPSK

Since QPSK is transmitting two bits simultaneously, so in order to achieve same symbol error probability as BPSK, QPSK must use twice the power of that of BPSK.

# 3. MULTIPLE-INPUT MULTIPLE-OUTPUT COMMUNICATIONS

This chapter presents the necessary background information about Multiple Input Multiple Output (MIMO) systems. The chapter is organized as follows. It begins with an introduction to a typical MIMO model and then describes the diversity exhibited by MIMO. It compares MIMO with single-input multiple-output (SIMO) and multiple input single-output (MISO) systems in terms of diversity, complexity and capacity.

A brief introduction to various relevant spatial multiplexing detection techniques and their comparisons with some simulations will be illustrated in the later part of the chapter.

## 3.1 Introduction to MIMO

Multiple-input multiple-output (MIMO) architecture has emerged as a popular solution to the continuous quest for increased capacity in modern wireless communication systems. It promises enormous capacity with a marginal increase in cost and complexity. This technology is now poised to penetrate large-scale commercial wireless products and networks such as broadband wireless access systems, wireless local area networks (WLAN), third-generation (3G) networks and beyond [11]. A MIMO system comprises a wireless communication link with multiple antenna elements in both transmitter and receiver as illustrated in figure 4 below.

Figure 4 : A MIMO Communication System Model

A vector of signals is transmitted from the transmitter antenna array simultaneously and then travels through the wireless channel. These signals are then received at the receiver antenna array which combines the signals in such a way that the quality of the communication in terms of Block Error Rate (BER) and data rate is significantly improved for each user.

MIMO system is based on a space-time signal processing architecture where time is complemented with space or distance which is obtained from the spatial distribution of antennas in the transmitter as well as the receiver. Space-time processing in MIMO systems basically increases data rate (spatial multiplexing) and link reliability (space-time coding).

An interesting feature of MIMO is that it exploits the multipath scenario, a serious pitfall of wireless transmission communication, to its advantage. MIMO benefits from it by transmitting data on multiple signal paths which increases the amount of information transferred in a system which in turn increases the number of users it can serve. Some of the key advantages of MIMO communication may be identified as follows. Extraordinary high spectral efficiency (from 30-40 bit/s/Hz) and large fade level reduction (10-30 dB) are the prime advantages [12]. Among other benefits that MIMO provides is a reduction in co-channel interference (5-15 dB), a flexible architecture through Digital Signal Processing (DSP) and diversity order, which is two times higher in MIMO than in SIMO.

### 3.1.1 MIMO System Equation

In a single user MIMO model with N transmit and M receive antennas, the MIMO system equation is given by

or in a matrix form

Where H is the channel matrix of size, r is the received signal vector, s is the transmitted signal vector, and n is an additive white Gaussian noise vector with zero mean and variance. The channel matrix H is the factor by which the signal is amplified and is also known as the channel coefficient. The element hij in the channel matrix H represents the complex gain between transmitter antenna j and receiver antenna i. The signal s can be a point from any constellation, but the BPSK signal constellation is used unless stated otherwise. Hence, and all the signals are independent.

### 3.1.2 Channel Model

The flat fading wireless channels are often categorized under two main groups, via Rayleigh and Rician channels. During the simulation process, both the Rayleigh and Rician cannel has been considered.

The Rayleigh channel is characterized as a channel in which fading occurs due to presence of multiple paths between the transmitter antenna and the receiver antenna, with no distinct dominant Line of Sight path. The importance of Rayleigh fading is that it represents the “worst case" scenario, where there no single or clear path exists between the transmitter and the receiver. It also represents a case that is mathematically predictable. In the MIMO environment, independent Rayleigh channels between pairs of antennas, with each  being a complex Gaussian with zero mean and unit magnitude variances are assumed.

Rician channel is a transmission channel that may have a line-of-sight component and several scattered waves from the multipath components. Rician channel is actually a model for radio propagation anomaly caused by partial cancellation of a radio signal by itself i.e. the signal arrives at the receiver by two different paths (hence exhibiting multipath interference), and at least one of the paths is changing (lengthening or shortening).

Rician fading occurs when one of the paths, typically a line of sight signal, is much stronger than the others. In Rician fading, the amplitude gain is characterized by a Rician distribution.

## 3.2 Spatial Multiplexing Detection

As mentioned earlier, MIMO exploits spatial multiplexing techniques in which multiple data streams are transmitted simultaneously and on the same frequency from the transmitter, which may or may not have the channel state information (CSI), using an antenna array. The detection operation at the receiver end of the MIMO link is called Spatial Multiplexing Detection (SMD). SMD is basically an operation in which the received signals are combined to obtain an estimate of the transmitted signal. SMDs are basically classified into two categories i.e. linear detection and non-linear detection.

### 3.2.1 Linear Detection

Linear detection is simple to implement on the receiver side and has less computational complexity. Thus it reduces the precious processing time in the receiver. However, these receivers have intermediate performance. Some of the common types of Linear Detection techniques are Selection Combining (SC), Equal Gain Combining (EGC), Maximum Ratio Combining (MRC), Zero Forcing (ZF), Linear Least Square Estimation (LLSE) and Minimum Mean Squared Error detection (MMSE).

Linear detection is a very simple process in which the received signal vector is multiplied with a weight matrix to obtain the estimate of the signal.

Here,  denotes the Hermitian transposition. The weight matrix  is chosen at our requirement. The weight matrix varies according to the particular linear detection scheme that has been employed. We should keep in mind to quantize the estimate  to produce the final estimate.

#### 3.2.1.1 Zero Forcing

Zero Forcing (ZF) is a linear spatial multiplexing detection scheme which is simple and very widely used in the receivers. As the name suggests, this scheme forces the interference to zero. However, it may sometimes result in noise inflation. The weight matrix for ZF is calculated using by

For a system with the same number of transmit and receive antennas (M = N) and

For a system with different numbers of antennas at the transmitter and receiver (M > N).

#### 3.2.1.2 Minimum Mean Squared Error

The performance of the detector can be improved in comparison to ZF if we can minimize both interference and noise at the same time. This can be done by the Minimum Mean Squared Error (MMSE) detection scheme, this is a tradeoff between noise inflation and interference suppression. The weight matrix for the MMSE detection is calculated by using the relation,

This is also equivalent to:

Here, IM is an M x M identity matrix and similarly IN  is also an N x N identity matrix respectively.

#### 3.2.1.3 Linear Least Square Error

Linear Least Square Error (LLSE) is also a linear spatial multiplexing detection scheme which is simple and can be widely implemented in the receivers. The estimate for the LLSE is calculated as:

Where  is the linear estimator given by

Here W is chosen to minimize

The LLSE matrix W is given by

The LLSE estimator does not eliminate the co-channel interference entirely since  does not equal the identity matrix, but the LLSE scheme has the desirable property of not enhancing noise as much as ZF estimation.

### 3.2.2 Optimal Detection

Maximum Likelihood (ML) is an optimal detection scheme. These types of detectors have a very high computational complexity and hence become the most time consuming detection process. Optimal detection is a non-linear process and basically, consisting of a thorough search through all possible combinations of signal vectors.

#### 3.2.2.1 Maximum Likelihood

ML is an optimal detection scheme that has very high computational complexity. This detection technique’s performance is superior compared to any other linear detection techniques but, it is the most time consuming detection procedure compared to others.

Moreover, the complexity increases with increase in the number of antennas or the size of the input signal constellation. ML minimizes the probability of error,

The probability of error, Pe is the probability of incorrectly estimating the signal block s. which can clearly be understood as, minimizing the probability of error is equivalent to maximizing the probability of correctly estimating the signal s.

The likelihood of the estimate  is obtained by minimizing the noise power, the ML estimate of s, i.e. is calculated by using the relation,

Thus, the ML detector chooses the message  which yields the smallest distance between the received vector candidates r, and hypothesized message.

# 4. V-BLAST ARCHITECTURE

In this chapter, a bandwidth efficient approach to wireless communication known as Vertical-Bell Labs Layered Space-Time (V-BLAST) architecture is introduced. The system overview of V-BLAST is presented along with a detailed description of the steps involved in the algorithm. Modifications to the classic V-BLAST technique in terms of estimation and ordering are described and the resulting technique is denoted as extended V-BLAST. The issue of optimal ordering in V-BLAST is dealt in the latter half of the chapter. The simulation results to compare ZF V-BLAST with other detection techniques are provided in chapter 6.

## 4.1 Introduction to V-BLAST

V-BLAST is a bandwidth efficient technique that utilizes the advantage of the spatial dimension in MIMO wireless system. V-BLAST technique exploits the multipath effect, which is the pitfall of traditional wireless communication, in order to achieve very high spectral efficiencies (bits/sec/Hz) [14].

The BLAST system was introduced by G.J.Foschini in 1996 in the form of a diagonally layered space-time architecture, which is now known as Diagonal BLAST (D-BLAST) [13]. D-BLAST has an elegant diagonally layered coding structure in which code blocks are dispersed across the diagonals in space-time. Though it promises rates near Shannon capacity, the diagonal approach due to its high complexity is difficult to realize physically. Later in 1998, Wolniansky et al [13] from Bell Laboratories presented a simplified version of BLAST which they called vertical BLAST or V-BLAST, which could be implemented in real-time in the laboratory. The essential difference between the two lies in the vector encoding process. In V-BLAST, the vector encoding process is simply a demultiplex operation followed by independent bit-to-symbol mapping of each substream.

V-BLAST splits a single user's data stream into multiple substreams and simultaneously transmits the data in parallel substreams through the transmit antenna array. All the substreams are transmitted in the same frequency band, so spectrum is used very efficiently. Thus, the effective transmission rate is increased by the number of antennas in transmit antenna array. The transmitted substreams travel through different paths and reach the receiver. At the receiver, there is an array of receive antennas which picks up the multiple transmitted substreams and their scattered images. Each antenna at the receiver receives a superimposed image of all transmitted substreams. Since the transmitted substreams originate from different transmit antennas which are situated at different points in the transmit array, the multiple substreams received are all scattered slightly differently. Using intelligent signal processing schemes at the receiver, these slight differences are utilized to identify and recover the substreams. Thus, the unavoidable multipath is exploited to provide a very useful spatial parallelism that is used to greatly improve data transmission rates [14].

Figure 5 : V-BLAST schematic diagram

V-BLAST is essentially a single user system which uses multiple transmitters but differs from the conventional single user system in the following aspects. The total channel bandwidth of BLAST is slightly more than the symbol rate. This is an advantage of BLAST system over other spread-spectrum multiple access techniques. Another benefit of BLAST is that each transmitted signal occupies only a fraction of bandwidth whereas in systems like FDMA each transmitted signal occupies the entire system bandwidth. Also, since there are spatially separated multiple antennas in V-BLAST system, the entire system bandwidth is used simultaneously by all of the transmitters all of the time unlike TDMA where each user gets a time slot to transmit its signal [13].

### 4.1.1 System Overview

A schematic block diagram of V-BLAST system is shown in Figure 5 consisting of N transmitters and M receivers. A single data stream is demultiplexed into N substreams, and each substream is then encoded into symbols and fed into respective transmitter. The power launched by each transmit antenna is proportional to so that the total radiated power is constant and independent of N.

The M receiving antennas on the receiver side also operate co-channel, each receiving the signals radiated from all N transmit antennas. In this thesis work, the channel is constructed for both Rayleigh flat fading and Rician Channel with matrix transfer function H, which is of size. The channel is assumed to be quasi-stationary i.e. channel time variation is negligible over a burst. Both BPSK and QPSK modulation has been considered during the simulation work.

## 4.2 V-BLAST Detection

The V-BLAST detection is referred to the detection method proposed by Wolniansky et al [13] from Bell Laboratories in 1998 and is a classic method. Considering a V-BLAST system with N transmit and M receive antennas in a Rayleigh / Rician fading environment, the data stream is partitioned into N sub streams, encoded and sent through different antennas at the transmitter end. Each receiver antenna receives the signals from all N transmit antennas. The received vector, assuming the vector of transmit symbols is given by can be expressed as

Where, n is a complex Gaussian noise vector with zero mean and magnitude variance  and H is a channel transfer matrix.

The method proposed for detection in [13] is linear combinational nulling. Each sub stream in turn is considered to be the desired signal, and the remainder is considered as “interferers". Nulling can be performed by simple linear algorithms like MMSE and ZF. These linear nulling approaches are viable but their performance is considerably lower than non-linear approaches. So nulling along with symbol cancellation is used for to obtain better performance from the detection technique.

The first and vital issue in the V-BLAST detection procedure is ordering. Since symbol cancellation is used later in detection, the order in which the components of s are detected becomes very important for overall system performance. Wolniansky et al [13] proposed an optimal ordering scheme for full ZF V-BLAST detection, where they describe a recursive procedure to obtain an ordered set A. This scheme is only optimal for ZF detection. Each element of the ordered set A is given by:

Where, G1 is the pseudoinverse of H and k1 is initialized as. All the elements of A are extracted as i runs from 1 to N-1. In the recursive process of detection, after a symbol is detected, a new pseudoinverse is computed for next iteration. This pseudoinverse is based on the ‘deflated’ version of the channel matrix H in which the column corresponding to the detected symbol is zeroed, i.e. where the superscript + denotes the pseudoinverse and subscript  indicates that column ki has been removed from H. The ordered set is hence presented as

This set is the permutation of integers from 1 to N specifying the order in which components of the transmitted symbol vector s are extracted.

After optimal ordering for the ZF V-BLAST detection, each symbol is decoded in three basic steps. First of all, decision statistic  is obtained using nulling vector.

Where r1=r is the received vector and wk1 is the nulling vector having the property

Where (H)j is the j-th column of H, and is the Kronecker delta.

The second step is slicing or quantizing yk1 to obtain.

Here, denotes the quantization operator for the constellation used. The third step is symbol cancellation. Here, assuming that ,is cancelled from the receiver vector r1, resulting in the modified vector r2.

.

Where is the k1-th column of. These three steps are performed for componentrecursively to obtain received vectors. Thus all the components of vector s are decoded.

# 5. METHODOLOGY

In this chapter, the algorithms that were followed throughout the thesis work will be described. ZF-VBLAST algorithm has been primarily focused in this chapter.

## 5.1 Overall Algorithm:

Step1:  Specify the number of the transmitter and receiver antenna

Step2: Specify SNR value

Step3: Sigma value (variance) for corresponding SNR

Step4: Find the length of Step 3

Step5: Generate the channel matrix

Step6: Generate BPSK or QPSK signal

Step7: Generate the noise

Step8: Generate the received signal

Step9: Estimate the received signal using the desired detection scheme

Step10: Compare the estimated signal with the generated signal

Step12: Monte Carlo simulation is done to find the bit error rate

Step13: Graph plotted for SNR Vs BER

## 5.2 ZF-VBLAST Algorithm

The processes involved in ZF VBLAST include ordering, interference nulling and interference cancellation. For the system with N transmit antenna and M receive antenna the received signal vector can be written as,

Here,  is  transmitted symbols, H is  channel matrix, n is the  noise matrix and r is  received signal. Every column of the channel matrix represents a transmitted symbol. Thus, removing a column of channel matrix is same as removing the effect of corresponding symbol. For example, removing column of the channel matrix is removing the effect of symbol. Similarly, the row of pseudo inverse of channel matrix also corresponds to the transmitted symbol.

### 5.2.1 Interference Nulling

Denoting the column of the channel by, the received signal can be expressed as,

Nulling is performed by linearly weighting the received symbols to satisfy the zero forcing criteria. The zero forcing nulling vector  is chosen such that

Then the decision static for  symbol is given by,

This decision is then quantized to obtain signal estimate.

### 5.2.2 Interference cancellation

The effect of the symbols already detected can be subtracted from the symbols that are yet to be detected. This improves the overall performance when the order of detection is carefully chosen. Denoting the received vector r by, if the nulling vector is, then the decision statistic for the ‘first’ symbol is,

If   is estimated after the decision then the interference due to  on the other symbols can be subtracted by taking

The next symbol is then detected by finding  and then making a decision on and so on.

### 5.2.3 Ordering

A simple ‘optimal’ ordering is based on the post detection SNR of each sub stream. The SNR for the detected symbol of vector r is given by

Here,  is the noise power and  denotes the expected value.As is seen that a smaller  value requires corresponding to  to have higher 2 norm. So the SNR for the sub stream is proportional to the norm of the column of H. Thus, the optimal detection order is in decreasing order of the 2 norm of the columns of H. The algorithm for ZF VBLAST is given below:

Initialize

- i =1

- G1= H+

- Find row in G1 with minimum norm i.e.

While all symbols are not detected, DO:

- : row of G matrix is taken as nulling   vector

- : interference nulling

- : symbol detection

- : interference cancelling

- Replace kith column of H with zero (0)

- Among non zero rows of Gi+1 ,find row with minimum norm i.e.

- i = i+1

- end

Here   represents the  column of the channel matrix and is the  row of the G matrix.

# 6. SIMULATION AND RESULTS

This thesis work is completely based in simulation and needs Monte Carlo simulation technique. Monte Carlo simulation techniques are a class of computational algorithms that rely on repeated random sampling to compute their results. It handles every complex and realistic system but has to repeat for each decision point.

For simulation purpose Matrix Laboratory (MATLAB) is used. MATLAB is a high-level language and interactive environment that enables to perform computationally intensive tasks faster than with traditional programming language. MATLAB is a numerical computing environment and fourth generation programming language. MATLAB allows matrix manipulation, plotting of functions and data, implementation of algorithms, creation of user interfaces, and interfacing with programs in other languages.

The channel is considered to be both Rayleigh and Rician channel; the modulation scheme taken into account is both BPKS and QPSK. We take the SNR range from -10 dB to 30 dB in step intervals of 5 dB. The block error rate is calculated by performing 1 million trials for each SNR value. The block error rate is then calculated for every SNR value. Performing 1million trials for each SNR value refers to repeatedly sending the same block of data 1million times from transmitter to the receiver for that SNR value. If the transmitted block of data doesn’t match with the detected or estimated data at the receiver then we can say that an error has occurs. We then calculate the total number of errors that has occurred during 1 million trials. The block error rate is then calculated for a SNR value as total number of error divided by total number of trials. As an example if total number of error is 5, 00,000 for 10, 00,000 trials at a SNR value then the block error rate for this SNR value is

A new channel is chosen in each trial and for each SNR value. Thus making the simulation very much similar to the Real Time data transfer where the channel cannot be determined beforehand.

## 6.1 Experimental Setup

During the experiment/simulation process, we first take into account the source with BPSK and QPSK modulation. In the case of BPSK modulation, each transmitter antenna can either transmit +1 or -1 i.e.  and similarly for the case of a QPSK modulation, each transmitter antenna can transmit either or i.e. . We assume that our MIMO system has N transmitting antennas and M receiving antennas. Thus the transmitted vectors can be expressed as.

After the desired symbols are transmitted by the antenna and just before receiving at the receiver side, these symbols pass through the channel. The channel considered during the experiment may either be a Rayleigh channel or a Rician Channel.

The Rayleigh channel is characterized as a channel in which fading occurs due to presence of multiple paths between the transmitter and receiver, there may be no distinct dominant path between them. The importance of Rayleigh fading is that it represents a worst case scenario, where there is not even a single clear path between the transmitter and the receiver.

Similarly in the case of a Rician Channel, a transmission channel there may be a line-of-sight component and several scattered waves from the multipath components. Rician channel is actually a model for radio propagation anomaly caused by partial cancellation of a radio signal by itself i.e. the signal arrives at the receiver by two different paths (hence exhibiting multipath interference), and at least one of the paths is changing (lengthening or shortening).

Rician fading occurs when one of the paths, typically a line of sight signal, is much stronger than the others. In Rician fading, the amplitude gain is characterized by a Rician distribution.

The  channel matrix is,

Here each is a complex Gaussian with mean zero and unit variance.

To make the simulation more realistic, noise is added to the transmitted signal and it is assumed that AWGN that has zero mean and variance. The noise matrix is of dimension and it is expressed as,

With these assumptions on transmitted signal, channel and noise, the received signal vector of size M by 1 can be written as,

The received signal r is then processed to find the best estimate of the transmitted symbols. The overall system setup is shown in figure 6 below.

Figure 6 :  Experimental setup for simulation purpose

## 6.2 Results

### 6.2.1 Results obtained from simulation with BPSK source at input.

Figure 7 : BER performance curve of ZF receivers in Rayleigh Channel

In figure 7, for ZF receivers, we can observe that as the number of Tx and Rx antennas increases, the BER increases for the Rayleigh channel.

Figure 8 : BER performance curve of ZF receivers in Rician Channel

In figure 8, for ZF receivers, we can observe that as the number of Tx and Rx antennas increases, the BER increases for the Rician channel.

Figure 9 : BER performance curve of MMSE receivers in Rayleigh Channel

In figure 9, for MMSE receivers, we can observe that as the number of Tx and Rx antennas increases, the BER decreases for the Rayleigh channel.

Figure 10 : BER performance curve of MMSE receivers in Rician Channel

In figure 10, for MMSE receivers, we can observe that as the number of Tx and Rx antennas increases, the BER decreases for the Rician channel.

Figure 11 : BER performance curve of LLSE receivers in Rayleigh Channel

In figure 11, for LLSE receivers, we can observe that as the number of Tx and Rx antennas increases, the BER increases for the Rayleigh channel.

Figure 12 : BER performance curve of LLSE receivers in Rician Channel

In figure 12, for LLSE receivers, we can observe that as the number of Tx and Rx antennas increases, the BER increases for the Rician channel.

Figure 13 : BER performance curve of ML receivers in Rayleigh Channel

In figure 13, for ML receivers, we can observe that as the number of Tx and Rx antennas increases, the BER decreases for the Rayleigh channel.

Figure 14 : BER performance curve of ML receivers in Rician Channel

In figure 14, for ML receivers, we can observe that as the number of Tx and Rx antennas increases, the BER decreases for the Rician channel.

Figure 15 : BER performance curve of ZF-VBLAST receivers in Rayleigh Channel

In figure 15, for ZF-VBLAST receivers, we can observe that as the number of Tx and Rx antennas increases, the BER decreases for the Rayleigh channel.

Figure 16 : BER performance curve of ZF-VBLAST receivers in Rician Channel

In figure 16, for ZF-VBLAST receivers, we can observe that as the number of Tx and Rx antennas increases, the BER decreases for the Rician channel.

### 6.2.2 Results obtained from simulation with QPSK source at input.

Figure 17 : BER performance curve of ZF receivers in Rayleigh Channel

In figure 17, for ZF receivers, we can observe that as the number of Tx and Rx antennas increases, the BER increases for the Rayleigh channel.

Figure 18 : BER performance curve of ZF receivers in Rician Channel

In figure 18, for ZF receivers, we can observe that as the number of Tx and Rx antennas increases, the BER increases for the Rician channel.

Figure 19 : BER performance curve of MMSE receivers in Rayleigh Channel

In figure 19, for MMSE receivers, we can observe that as the number of Tx and Rx antennas increases, the BER decreases for the Rayleigh channel.

Figure 20 : BER performance curve of MMSE receivers in Rician Channel

In figure 20, for MMSE receivers, we can observe that as the number of Tx and Rx antennas increases, the BER decreases for the Rician channel.

Figure 21 : BER performance curve of LLSE receivers in Rayleigh Channel

In figure 21, for LLSE receivers, we can observe that as the number of Tx and Rx antennas increases, the BER increases for the Rayleigh channel.

Figure 22 : BER performance curve of LLSE receivers in Rician Channel

In figure 22, for LLSE receivers, we can observe that as the number of Tx and Rx antennas increases, the BER increases for the Rician channel.

Figure 23 : BER performance curve of ML receivers in Rayleigh Channel

In figure 23, for ML receivers, we can observe that as the number of Tx and Rx antennas increases, the BER decreases for the Rayleigh channel.

Figure 24 : BER performance curve of ML receiver in Rician Channel

In figure 24, for ML receivers, we can observe that as the number of Tx and Rx antennas increases, the BER decreases for the Rician channel.

Figure 25 : BER performance curve of ZF-VBLAST receivers in Rayleigh Channel

In figure 25, for ZF-VBLAST receivers, we can observe that as the number of Tx and Rx antennas increases, the BER decreases for the Rayleigh channel.

Figure 26 : BER performance curve of ZF-VBLAST receiver in Rician Channel

In figure 26, for ZF-VBLAST receivers, we can observe that as the number of Tx and Rx antennas increases, the BER decreases for the Rician channel.

### 6.2.3 Comparison of Linear / Optimal / VBLAST with BPSK source.

Figure 27 : BER performance curve in Rayleigh Channel for 2-2 MIMO link

In figure 27, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 2-2 MIMO link with BPSK source.

Figure 28 : BER performance curve in Rician Channel for 2-2 MIMO link

In figure 28, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 2-2 MIMO link with BPSK source.

Figure 29 : BER performance curve in Rayleigh Channel for 3-3 MIMO link

In figure 29, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 3-3 MIMO link with BPSK source.

Figure 30 : BER performance curve in Rician Channel for 3-3 MIMO link

In figure 30, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 3-3 MIMO link with BPSK source.

Figure 31 : BER performance curve in Rayleigh Channel for 4-4 MIMO link

In figure 31, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 4-4 MIMO link with BPSK source.

Figure 32 : BER performance curve in Rician Channel for 4-4 MIMO link

In figure 32, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 4-4 MIMO link with BPSK source.

Figure 33 : BER performance curve in Rayleigh Channel for 5-5 MIMO link

In figure 33, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 5-5 MIMO link with BPSK source.

Figure 34 : BER performance curve in Rician Channel for 5-5 MIMO link

In figure 34, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 5-5 MIMO link with BPSK source.

### 6.2.4 Comparison of Linear / Optimal / VBLAST with QPSK source.

Figure 35 : BER performance curve in Rayleigh Channel for 2-2 MIMO link

In figure 35, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 2-2 MIMO link with QPSK source.

Figure 36 : BER performance curve in Rician Channel for 2-2 MIMO link

In figure 36, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 2-2 MIMO link with QPSK source.

Figure 37 : BER performance curve in Rayleigh Channel for 3-3 MIMO link

In figure 37, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 3-3 MIMO link with QPSK source.

Figure 38 : BER performance curve in Rician Channel for 3-3 MIMO link

In figure 38, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 3-3 MIMO link with QPSK source.

Figure 39 : BER performance curve in Rayleigh Channel for 4-4 MIMO link

In figure 39, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 4-4 MIMO link with QPSK source.

Figure 40 : BER performance curve in Rician Channel for 4-4 MIMO link

In figure 40, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 4-4 MIMO link with QPSK source.

Figure 41 : BER performance curve in Rayleigh Channel for 5-5 MIMO link

In figure 41, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 5-5 MIMO link with QPSK source.

Figure 42 : BER performance curve in Rician Channel for 5-5 MIMO link

In figure 42, for comparison of linear, optimal and V-BLAST receivers, we can observe least BER value for ML detectors in a 5-5 MIMO link with QPSK source.

### 6.2.5 Performance comparison of modulation techniques for different channels.

Figure 43 : BER performance curve of ZF detector in Rayleigh Channel

In figure 43, we can observe least BER value for ZF detectors with BPSK source.

Figure 44 : BER performance curve of ZF detector in Rician Channel

In figure 44, we can observe least BER value for ZF detectors with BPSK source.

Figure 45 : BER performance curve of MMSE detector in Rayleigh Channel

In figure 45, we can observe least BER value for MMSE detectors with BPSK source

Figure 46 : BER performance curve of MMSE detector in Rician Channel

In figure 46, we can observe least BER value for MMSE detectors with BPSK source

Figure 47 : BER performance curve of LLSE detector in Rayleigh Channel

In figure 47, we can observe least BER value for LLSE detectors with BPSK source.

Figure 48 : BER performance curve of LLSE detector in Rician Channel

In figure 48, we can observe least BER value for LLSE detectors with BPSK source.

Figure 49 : BER performance curve of ML detector in Rayleigh Channel

In figure 49, we can observe least BER value for ML detectors with QPSK source.

Figure 50 : BER performance curve of ML detector in Rician Channel

In figure 50, we can observe least BER value for LLSE detectors with QPSK source.

Figure 51 : BER performance curve of ZF-VBLAST detector in Rayleigh Channel

In figure 51, we can observe least BER value for ZF-VBLAST detectors with BPSK source.

Figure 52 : BER performance curve of ZF-VBLAST detector in Rician Channel

In figure 52, we can observe least BER value for ZF-VBLAST detectors with BPSK source.

### 6.2.6 Performance comparison in terms of channel with different modulation schemes.

Figure 53 : BER performance curve of ZF detector with BPSK source

In figure 53, we can observe least BER value for ZF detectors in Rician Channel.

Figure 54 : BER performance curve of ZF detector with QPSK source

In figure 54, we can observe least BER value for ZF detectors in Rician Channel.

Figure 55 : BER performance curve of MMSE detector with BPSK source

In figure 55, we can observe least BER value for MMSE detectors in Rician Channel.

Figure 56 : BER performance curve of MMSE detector with QPSK source

In figure 56, we can observe least BER value for MMSE detectors in Rician Channel.

Figure 57 : BER performance curve of LLSE detector with BPSK source

In figure 57, we can observe least BER value for LLSE detectors in Rician Channel.

Figure 58 : BER performance curve of LLSE detector with QPSK source

In figure 58, we can observe least BER value for LLSE detectors in Rician Channel.

Figure 59 : BER performance curve of ML detector with BPSK source

In figure 59, we can observe least BER value for ML detectors in Rician Channel.

Figure 60 : BER performance curve of ML detector with QPSK source

In figure 60, we can observe least BER value for ML detectors in Rician Channel.

Figure 61 : BER performance curve of V-BLAST detector with BPSK source

In figure 61, we can observe least BER value for V-BLAST detectors in Rician Channel.

Figure 62 : BER performance curve of V-BLAST detector with QPSK source

In figure 62, we can observe least BER value for V-BLAST detectors in Rician Channel.

# 7. DISCUSSION

The simulation results that are shown in chapter 6 are limited only for 2 by 2, 3 by 3, 4 by 4 and 5 by 5 MIMO link system. The performance of the various detectors can be analyzed from the obtained simulation results. The performances of various detectors are analyzed by studying the BER versus SNR plot. The individual plots are then compared against each other for the comparison study.

The simulations are performed following the experimental setup as described in chapter 6.1. Every plot is obtained after 1 million iterations for each SNR value. The detector that has the minimum BER for all SNR value is considered to demonstrate the best performance for the considered channel model.

After the comparative performance analysis of figure 7, 8, 17 and 18 it can be observed that the performance of ZF detectors degrade as the number of antennas increases. The LLSE detectors also show the similar behavior, this can be observed from the comparative performance analysis of figure 11, 12, 21 and 22.

In contrast, the MMSE detector exhibits the contrasting behavior compared to ZF and LLSE detectors. After comparative performance analysis of figure 9, 10, 19 and 20 we can observe that as number of antennas increase, the performance of MMSE detector drastically improves. Similarly, comparing the performance analysis of ML, referring to figure 13, 14, 23 and 24, it can be observed that as the number of antennas in ML detectors increases, the performance of the receiver improves. The similar results can be observed for the V-BLAST detectors in figure 15, 16, 25 and 26. As the number of antennas increase, the performance can be seen to improve drastically.

In our case, the ML detector satisfies the criterion for optimal detector for MIMO system taking Rayleigh or Rician channel and considering both the BPSK or QPSK sources. Hence ML is the optimum detector. Although the performance of this detector is excellent, the computational complexity is relatively very high for ML detectors compared to other detectors. This can be observed in the results obtained from figure 27 to figure 42 for different MIMO detectors under Rayleigh and Rician channel.

Similarly, the BER for the ZF and LLSE detector is the highest for each SNR value as compared to other detectors so it has the worst performance for both the Rayleigh and Rician channel. Likewise, from these figures, we can observe that the performance of LLSE and ZF detectors are very much identical. Also, it can be observed that the performance of MMSE detector is in the midway between the linear and optimal detectors.

The decoding schemes (ZF, MMSE, LLSE and ZF-VBLAST) worked best i.e. it showed least BER value with BPSK source for both the Rayleigh and Rician channel. Whereas, the ML decoding scheme resulted least BER value while QPSK source was used at the input. This can be seen in the plots in figure 43 to figure 52.

Finally, in the performance comparison for different channels under the BPSK and QPSK modulation can be observed in figure 53 to figure 64, after analysis, we can observe that all the detectors (ZF, LLSE, MMSE, ML and V-BLAST) yield least BER value for both the BPSK and QPSK modulation technique when the Rician channel was used.

# 8. LIMITATION

This thesis primarily focused on the performance analysis and comparison of various MIMO detectors. Every work has its own limitation so this thesis too has also some limitations.

The simulation results shown are limited only for the MIMO system having same number of antennas at the transmitter and at the receiver.

The simulation considers that the modulation technique used at the transmitter side is either BPSK or QPSK. Higher modulation techniques can be implemented in order to obtain high data rate.

To obtain the results, 1 million iterations were performed for each SNR values; we can obtain better result with large number of iteration at each SNR value.

In the results the plots were overlapping this is also a limitation of the simulation work.

# 9. CONCLUSION

The simulations resulted that LLSE and ZF scheme had somewhat similar performance. The ZF and LLSE schemes were observed to have the worst performance among all the detection schemes, and the performance of the MMSE detector laid in-between LLSE, ZF and ML detector.

The performance of ZF VBLAST was observed to be in mid-way between the linear detectors (ZF, LLSE and MMSE detector) and optimum detectors (ML detector). The simulation resulted that the ZF-VBLAST detectors had least BER values as the number of transmitting and receiving antennas were increased.

The performance comparison plots for linear versus optimum versus ZF-VBLAST provided in chapter 6 resulted that the ML detector had the best performance in terms of BER among all other detectors being an optimal detection scheme for any chosen modulation (i.e. BPSK or QPSK) schemes and taking Rayleigh or Rician channel into consideration.

The BER of the MIMO system completely depended upon the number of transmitting antennas and receiving antennas used in the system. It was observed that the performance of the ZF and LLSE detectors degraded as the number of transmitting and receiving antennas increased. In contrast, the performance of ML, MMSE and ZF-VBLAST detectors greatly improved as the number of transmitting and receiving antennas increased.

The simulation for the performance analysis of different modulation schemes resulted that the ZF, LLSE, MMSE and ZF-VBLAST detectors had the least BER value for BPSK modulated source at the input for both the Rayleigh and Rician channel. Whereas, only the ML detectors had the least BER value while QPSK source was used at the input for both the Rayleigh and Rician channels.

The simulation for the performance comparison of different channels resulted that all the detectors (ZF, LLSE, MMSE, ML and ZF-VBLAST) had the least BER value for Rician channel for both BPSK and QPSK modulation scheme.

# 10. FUTURE RECOMMENDATIONS

There are many possible extensions that can be done to the works presented in this thesis. Some important fields in which future work can be extended are described in this chapter.

## 10.1 Approach suitable for higher constellations

A noticeable extension of this thesis work is the investigation for the performance of detection schemes proposed in this thesis for higher signal constellations. The results presented here assume either BPSK or QPSK modulation at the transmitter side. An immediate need is to implement these detection schemes using higher signal constellations like 16- QAM, 64-QAM etc.

## 10.2 Investigations for other fading channels

Another extension is the investigation for the performance of the detection schemes besides the ones described in this thesis work. The Rayleigh and Rician fading channel has been described in this thesis work. Other channels like Additive White Gaussian Noise (AWGN) channel can also be analyzed using the similar approach.

## 10.3 Group detection

Another possible extension could be the implementation of group detection techniques in V-BLAST receivers. Instead of detecting one symbol and canceling it out to detect another symbol at each recursive step, a group of symbols can be detected and canceled out to detect the rest. This will help in accelerating the V-BLAST detection procedure.

## 10.4 Ordering

Ordering is an important step in VBLAST detection. Future work can be done to find new optimal ordering technique.

# References

[1]	A. F. Naguib, N. Seshadri, and A. R. Calderbank, “Increasing Data Rate Over Wireless Channels," IEEE Signal Processing Mag., pp. 76-92, May2000.

[2]	Siavash M. Alamouti “A Simple Transmit Diversity Technique for Wireless communications” IEEE Select areas in communication VOL 16 No8 october1998.

[3]	Hamid Jafarkhani, “Space time coding theory and practice,” Cambridge University, 2005.

[4]	David Tse, Pramod Viswanath, “Fundamentals of wireless communication,” Cambridge University Press, 2005.

[5]	A.Lozano,F.R. Farrokhi and R A Valenzuela, “Lifting the limits on high-speed wireless data access using antenna arrays” IEEE Commun.Mag, pp156-162, Sept 2001.

[6]	J. Paulraj and C. B. Papadias, “Space-Time Processing for Wireless Communications,” IEEE Signal Process. Magazine, pp. 49-83, November 1997.

[7]	Z. Liu, G. B. Giannakis, A. Scaglione, and S. Barbarossa, “Decoding and equalization of unknown multipath channels based on block precoding and transmit antenna diversity,” in Proc. 33rd Asilomar Conf. Sig., Syst. Comput., 1999, pp. 1557–1561.

[8]	S. Shahbazpanuni, M. Beheshti, A.B. Gershman, M. Gharavi and K. M. Wong, “Minimum Variance Linear Receivers for Multiaccess MIMO Wireless Systems with Space-Time Block Coding,” IEEE Trans. Signal Process.,vol. 52, pp. 3306-3312, December 2004.

[9]	H.Hourani, “An overview of diversity techniques in wireless communication systems” IEEE JSAC, pp. 1200-5, October 2004.

[10] 	Balaban, N. and Salz, “Dual diversity combing and equalization in digital cellular mobile radi,” IEEE Trans on Vechicular Technology, May 1994.

[11]	X. Wang and H. Poor, Wireless Communication Systems: Advanced Techniques for Signal Reception, 1st ed. New York: Prentice Hall PTR, 2003.

[12]	G. D. Golden, G. J. Foschini, R. A. Valenzuela, and P. W. Wolniansky, “Detection algorithm and initial laboratory results using the v-blast space-time communication architecture,” Electron. Lett., vol. 35, no. 1, pp. 14-15, Jan. 1999.

[13]	P. W.Wolniansky, G. J. Foschini, G. D. Golden, and R. A. Valenzuela, “V-BLAST: An architecture for realizing very high data rates over the rich-scattering wireless channel," in Proc. Int. Symp. Signals, Systems,and Electronics (ISSSE'98), Pisa, Italy, Sept. 29 1998.

[14]	Lucent Technologies, “http://www.bell-labs.com/project/blast/high-level-overview.html," 2000.

[15]	Stüber, G. L., 2000. “Principles of Mobile Communication,” Kluwer Academic Publishers.

[16]	Charan Langton  “All about modulation,”  2006.

[17]	M. Khatiwada, “A Brief Overview of MIMO Wireless Communication as a Significant Technical Breakthrough in Modern Communications” in SCITECH.

[18]	D. Gesbert, M. Shafi, D. Shiu, P. Smith, A. Naguib, “From Theory to Practice: An Overview of MIMO Space-Time Coded Wireless Systems”, IEEE Journal on Select Areas in communication, Vol.21, No.3, pp.281-302, April, 2003.

[19]	Yavuz Yapici, “V-BLAST/MAP: A NEW SYMBOL DETECTION ALGORITHM FOR MIMO CHANNELS” Master’s Degree Thesis, Bilkent University, Turkey, January, 2005.

[20]	Fenghua Li, “Performance analysis of VBLAST detector for the MIMO channel”, Master's Degree Project, Stockholm, Sweden, 2007-06-21.

[21]	G. Lawton, “Is MIMO the future of wireless communications?" IEEE Computer. vol. 37, no. 7, pp. 20-22, July 2004.

[22]	Foschini, G. J. and Gans, M. “On the limits of wireless communication in a fading environment when using multiple antennas” Wireless Pers. Commun., 6: Mar. 1998

# Bibliography

[1]	Simon Haykin, “Digital Communications”, fourth edition.

[2]	John G. Proakis, “Digital Communication”, fourth edition.